## Slide 1: Cheese production

## Slide 2: Objective
To explain the process of secondary milk processing to make Cheddar cheese.

## Slide 3: Cheese production
In this cheese factory, up to 25,000 litres of milk can be delivered from dairy farms at any one time.
The milk is unloaded and literage is checked before the milk is transferred into silos.

## Slide 4: Pasteurisation
The first process the milk goes through is pasteurisation.
Pasteurisation reduces the number of spoilage microorganisms and provides a good environment for the starter cultures to grow.
Milk is cooled in a vat after pasteurisation to 32 °C, an ideal temperature for the starter culture to grow.

## Slide 5: Curdling
A starter culture, similar to freeze dried natural yogurt, is then added to the pasteurised milk. This begins to acidify the milk.
The curlding step allows the bacteria to grow and begin fermentation.
Rennet, an enzyme that acts on the milk protein caesin, is added and the milk coagulates, forming lumps.
The milk is mixed and then left to settle, while the junket forms, where the milk curdles and separates into curds and whey.

## Slide 6: Cooling tables and draining whey
The curds and whey run from the cheese vat onto the cooling tables.
The cooling tables are used to:
1) cool the curds and whey;
2) separate the curds from the whey.
The whey is drained off for further processing where cream is removed from the whey by centrifuge and made into butter.
Protein is also extracted from the whey for different ingredients. In addition, lactose is removed from the water and then used for animal feed.

## Slide 7: Cheddaring
The mixture is moved around on the cooling tables allowing the whey to drain out through a central perforated channel.
As the liquid is drained off a solid mass is created, called curd mats.

## Slide 8: Cheddaring
The curd mats are cut into sections and piled on top of each other and turned periodically.
This step is called ‘cheddaring’.

## Slide 9: Salting
Around 1,900 kg of cheese can be made on the cooling table within an hour.
The curd pieces are fed into a mill and sliced into pieces about half the size of a thumb. This ensures the salt can be uniformly mixed throughout the curd.
Salt is added to act as a preservative and prevent the cheese from going rancid during the maturing process. It also adds flavour to the cheese.

## Slide 10: Cheese blocks
The mixture is then taken into a six metres high tower to form rectangular shaped cheese blocks, weighing 20 kilograms each. After confirming the weight, these blocks are individually identified, ensuring traceability.
Following this, the blocks are vacuum packaged and encased in six or seven wooden boards.
They are then taken to the cool room and are chilled to a temperature of 10-12°C.

## Slide 11: Cheese ripening
In the cool room, acidification of cheese continues at a much slower rate; this period is known as ripening.
When it is time to select the cheese, the grader decides which cheeses are the best eaten young and which should be left to ripen (for up to 18 months) developing the special features and flavours associated with West Country Farmhouse Cheese.

## Slide 12: Cheese packaging
The final stage in cheese production is slicing and packaging.
The cheese blocks are then cut into specific sizes, packaged and labelled. These products are sold via retailers large and small throughout the UK, as well as in the farm shop.

## Slide 13: Protected names
Three European Union schemes of geographical indications and traditional specialties promote and protect names of quality agricultural products and foodstuffs.
They are known as:
Protected designation of origin (PDO);
Protected geographical indication (PGI);
and Traditional specialities guaranteed (TSG)

## Slide 14: Protected names
The protected name of the cheese being made is West Country Farmhouse Cheddar.
The conditions are:
The cheddar is made using milk from local herds reared and milked in the four Counties (Cornwall, Devon, Somerset, Dorset);
The cheddar contains no colouring, flavouring or preservatives;
The cheddar is made in these four counties to traditional methods, e.g. cheddaring;
The cheddar is made and matured on the farm and aged for at least 9 months.

## Slide 15: By-products from the farm
In addition to the cheese, there are other products produced on the farm. The male calves are kept to form a herd of beef animals supplying quality meat to the farm shop.
Arable crops, including wheat, barley, oats, oilseed rape and maize is grown. Some of the grain is used to feed the stock, such as dairy cows and pigs, while the rest is sold.
Pigs are fed on whey from the cheese production and cereals grown on the farm.

## Slide 16
For further information, go to:
www.foodafactoflife.org.uk